## Slide 1: Aircraft observations of NH3 from industrial and agricultural sources Lara Noppen, Lieven Clarisse, Frederik Tack, Thomas Ruhtz, Alexis Merlaud, Martin Van Damme, Michel Van Roozendael, Dirk Schuettemeyer and Pierre Coheur
NH3 HRI distribution from IASI measurements

## Slide 2: The global nitrogen cycle
Chart: Trends in emissions in the EU-27 (indexed to 2005)
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
NH_3 | 1 | 0.991 | 0.997 | 0.973 | 0.953 | 0.944 | 0.935 | 0.933 | 0.93 | 0.935 | 0.945 | 0.95 | 0.954 | 0.943 | 0.92 | 0.913
Nox | 1 | 0.976 | 0.948 | 0.885 | 0.817 | 0.798 | 0.77 | 0.738 | 0.707 | 0.68 | 0.669 | 0.649 | 0.636 | 0.612 | 0.578 | 0.515
NH3
NO2
European Environment Agency, https://www.eea.europa.eu/data-and-maps/daviz/trends-in-eu-27-emissions-1#tab-googlechartid_chart_11
Key forms of reactive nitrogen (Nr) :
  Nitrogen dioxide (NO2)
  Ammonia (NH3)
Anthropogenic emissions of Nr disturb the global nitrogen cycle  devastating consequences to biodiversity, soil, water, and air quality
Effective monitoring is needed !
Chart: NH3 sources
| Agriculture | Natural | Biomass burning | Other
Sources | 0.6 | 0.2 | 0.1 | 0.1

## Slide 3: Satellite observations of NH3
Global distribution of NH3 columns from 11 years of IASI measurements  importance of point sources
Van Damme, M. et al. (2018). Industrial and agricultural ammonia point sources exposed. Nature, 564(7734): 99–103.
Fertilizer plant
Poultry housing
IASI sounder

## Slide 4: Limitations of current satellite measurements
Nitrosat
  Satellite mission proposed for the 11th ESA's Earth Explorer call (phase 0)
  Simultaneous observations of NO2 and NH3 at < 500 m resolution
NITROCAM
  Airborne measurements of both species at very high spatial resolution
Spatial resolution of current satellites too coarse (~ 10 km)
Poultry
Pigs
Mixed
IASI measurements of NH3
Concentrated Animal Feeding Operation
Coheur, P. et al. (2020). NITROSAT : Mapping reactive nitrogen at the landscape scale. Technical report.
z
y
x
Fertilizer plant

## Slide 5: NITROCAM campaigns
Instruments on board the aircraft Cessna 207T:
  SWING  NO2
  Hyper-Cam LW  NH3
 | SWING | Hyper-Cam LW
Wavelength range | 280 – 550 nm | 800 – 1350 cm-1
Spectral resolution (FWHM) | 0.7 nm | 1.2 – 1.6 cm-1
FOV across-track | 100° | 25.7° max
IFOV across track | 3° | 0.08°
Swath width | 2900 m | 1350 m
Ground speed | 60 m.s-1 | 51 m.s-1
Exposure time | 0.5 s | 2.29 s
Spatial resolution | 170 m | 5 m
Weight | 3 kg | 140 kg
Size (L x W x H) | 20 x 20 x 30 cm3 | 100 x 60 x 50 cm3
Scanning | Whiskbroom | Imaging Fourier interferometer
Target platform | UAV/aircraft | Aircraft
Hyper-Cam LW
SWING

## Slide 6: NITROCAM campaigns
Germany flights
Italy flights
(2020-2021)
(2022)

## Slide 7: Germany flights
08-10-20 | Piesteritz
13-11-20 | Reuter West
13-11-20 | Schwarze Pumpe
24-11-20 | Piesteritz
24-11-20 | Schwarze Pumpe
28-04-21 | Piesteritz
09-05-21 | Staßfurt
10-05-21 | Magdeburg
31-05-21 | Berlin
14-06-21 | Berlin
09-10-21 | Berlin
24-10-21 | Berlin
Piesteritz
Staßfurt
Berlin
Magdeburg

## Slide 8: Germany flights
08-10-20 | Piesteritz
28-04-21 | Piesteritz
09-05-21 | Staßfurt
Piesteritz
Staßfurt
Berlin
Magdeburg

## Slide 9: Germany flight – Piesteritz
Flight over the industrial site of Piesteritz in autumn 2020
Measurements of NH3 by the Hyper-Cam instrument in the infrared at a spatial resolution of 4 m
Mean spectrum
Solar panels

## Slide 10: Piesteritz – NH3 plume
Detection of NH3 with the HRI method (or matched filter)
HRI = 0
HRI < 0
HRI > 0

## Slide 11: Piesteritz – Various satellite footprints
Progressive degradation of the spatial resolution of HRI distribution
Sub-km spatial resolution required to identify the point source
-10 -6 -2 0 2 6 10
HRI
-10 -6 -2 0 2 6 10
HRI
-10 -6 -2 0 2 6 10
HRI
-3 -2 -1 0 1 2 3
HRI
12 m
200 m
500 m
2000 m
Nitrosat

## Slide 12: Deriving point source emission rates
Two most accurate and practically applicable approaches
Jacob, D. J., et al. (2022). Quantifying methane emissions from the global scale down to point sources using satellite observations of atmospheric methane, Atmos. Chem. Phys., 22, 9617–9646.

## Slide 13: Deriving point source emission rates
Two methods used to derive emission fluxes from the plant:
Point source
Mass of NH3 within the slice
Time for the plume to travel the slice
Residence lifetime of NH3 within the plume
Total mass of NH3 within the plume
Integrated mass enhancement (IME)
Cross-sectional flux (CSF)
Deposition and chemical loss
U

## Slide 14: Deriving point source emission rates
Two methods used to derive emission fluxes from the plant:
Point source
Mass of NH3 within the slice
Time for the plume to travel the slice
Residence lifetime of NH3 within the plume
Total mass of NH3 within the plume
Integrated mass enhancement (IME)
Cross-sectional flux (CSF)
 Adapted for downsampled data
Deposition and chemical loss
Sum of the NH3 masses calculated for each weighted pixel between two traverses
U

## Slide 15: Piesteritz – Emission rate retrievals
General behavior of the plume  Gaussian model
NH3 profile
Plume altitude
Wind
Vertical dispersion
Initial buoyancy flux

## Slide 16: Piesteritz – Emission rate retrievals
General behavior of the plume  Gaussian model
Emission rate retrieval :
  With the IME method
  With the CSF method
  From native measurements and data downsampled at 200 m and 500 m resolutions
IME | 1600 t.yr-1
CSF – 200 m | 2500 t.yr-1
CSF – 500 m | 2500 t.yr-1
CSF – native | 2200 t.yr-1
E-PRTR | 400 t.yr-1

## Slide 17: Germany flight – Piesteritz
Second flight over Piesteritz in spring 2021
Fertilizer plant
IME | 1600 t.yr-1
CSF – 200 m | 2500 t.yr-1
CSF – 500 m | 2500 t.yr-1
CSF – native | 2200 t.yr-1

## Slide 18: Piesteritz – Simultaneous NH3 / NO2 plumes
NH3 detected in the infrared
Fertilizer plant
Fertilizer plant
NO2 detected in the UV-vis

## Slide 19: Germany flight – Staßfurt
Flight over a large area in Staßfurt in spring 2021
Detection of various NH3 industrial sources
Wool production factory
Soda ash plant
Sugar factory
Soda ash plant

## Slide 20: Staßfurt – Sedimentation basins
Including the sedimentation basins associated with the soda ash plant of Staßfurt
Not in the E-PRTR register
Confirmation with the whitening technique
Soda ash plant
Wool production factory
Soda ash plant
Sugar factory

## Slide 21: Staßfurt – Sedimentation basins
Including the sedimentation basins associated with the soda ash plant of Staßfurt
Not in the E-PRTR register
Confirmation with the whitening technique
Soda ash plant
Wool production factory
Soda ash plant
Sugar factory

## Slide 22: Italy flights
Este
Ravenna
Mantua
Grosseto
Livorno
Rosignano
Parma
Modena
13-05-22 | Mantua
14-05-22 | Grosseto (experiment)
15-05-22 | Grosseto
17-05-22 | Grosseto
19-05-22 | Rosignano
20-05-22 | Este
18-06-22 | Mantua
20-06-22 | Livorno
21-06-22 | Ravenna (part 1)
22-06-22 | Ravenna (part 2)
24-06-22 | Modena
26-06-22 | Mantua (night)
27-06-22 | Ravenna (north)
30-06-22 | Parma

## Slide 23: Italy flights
Este
Ravenna
Mantua
Grosseto
Livorno
Rosignano
Parma
Modena
13-05-22 | Mantua
14-05-22 | Grosseto (experiment)
15-05-22 | Grosseto
17-05-22 | Grosseto
19-05-22 | Rosignano
18-06-22 | Mantua
26-06-22 | Mantua (night)
30-06-22 | Parma

## Slide 24: Italy flights – NH3 sources
The Po Valley is the highest hotspot of NH3 in Europe
NH3 observed from IASI
NH3 emissions included in the E-PRTR inventory
Intensive livestock production and aquaculture
Chemical industry
Waste and wastewater management
Mineral industry
Paper and wood production processing
 agriculture

## Slide 25: Italy flight – Rosignano
NITROCAM – 12 m
Soda ash plant
Nitrosat – 500 m
Flight over the soda ash plant of Rosignano in spring 2022

## Slide 26: Italy flight – Mantua
Flight over the agricultural area of Mantua in spring 2022
NH3 distribution from 2 years of IASI measurements

## Slide 27: Italy flight – Mantua
Flight over the agricultural area of Mantua in spring 2022
Farm
Farm
Farm
Farm
Chipboard producing

## Slide 28: Italy flight – Mantua
Nitrosat – 500 m
Flight over the agricultural area of Mantua in spring 2022
Farm
Farm
Farm
Farm
Chipboard producing

## Slide 29: Italy flight – Mantua
Flight over Mantua during nighttime
What is expected :
  TC = Tsurf – Tair < 0
  Emission spectra
  HRI < 0
Average TC
- 5.55 K
IASI measurements

## Slide 30: Italy flight – Parma
Flight over the region of Parma
NH3 distribution from 2 years of IASI measurements

## Slide 31: Italy flight – Parma
Flight over the region of Parma
Gradient of NH3

## Slide 32: Italy flight – Parma
Flight over the region of Parma
Gradient of NH3
IASI measurements
NITROCAM - 12 m
Nitrosat - 500 m

## Slide 33: Italy flight – Grosseto
Flight over a fertilizer experiment in Grosseto

## Slide 34: Italy flight – Grosseto
Flight over a fertilizer experiment in Grosseto
NITROCAM – 12 m
Nitrosat – 500 m

## Slide 35: Grosseto – One day after the release
Greenhouses
Cows
Lagoons

## Slide 36: Grosseto
Greenhouses
Cows
Lagoons
One day after the fertilizer experiment
Three days after the fertilizer experiment
NITROCAM – 12 m

## Slide 37: Grosseto
Degradation of the spatial resolution at 500 m
Detection of one plume coming from the farm
One day after the fertilizer experiment
Three days after the fertilizer experiment
Nitrosat – 500 m
Nitrosat – 500 m

## Slide 38: Conclusions
Limitation of current sounders for observing/estimating NH3 emissions
 the satellite Nitrosat
 supported by the NITROCAM aircraft campaigns
The driving uncertainty for quantifying emissions : the plume behavior
Some small industrial point sources will be missed at 500 m resolution
Individual farms and freshly fertilized fields can be detected
Multiple overpasses needed to constrain emissions on an individual farm level and to distinguish point sources from fertilized field

## Slide 39: Thank you!