## Slide 1: Inversion of radiative transfer model ‘INFORM’
Clement ATZBERGER EUFAR/DLR 12 July 2017

## Slide 2: BOKU - University of Natural Resources & LiFe Sciences
History: … since 1875
Staffing: … ca. 20
Teaching: … several bachelor & master programs
Thematics: … Remote sensing & photogrammetry … GIS & land information … Surveying & geodesy
Notes: Two cooperate slides
Current position
Previous working places

## Slide 3: Remote Sensing Group at BOKU Key competencies
Photo- grammetry
BRDF modeling
Laser scanning
RS data assimilation
Time series analysis
LULC mapping
Land surface phenology
Drought monitoring
Precision agriculture
Biophysical parameter
RT modeling

## Slide 4
Schlerf et al. 2005
Mapping of vegetation traits
Traditional (empirical) modeling:
“Learning from training samples”
Advantages: - Often high accuracy
- Simple to implement
Notes: Hyperspektral Statistische Verfahren: Data mining
Linear regression between best narrowband PVI and LAI. Values of R2 and RMSE are cross-validated. When the outlier at position 4.1/-0.104 is removed, cross-validated R2 increases to 0.77 and RMSE decreases to 0.54 m2 m-2

## Slide 5
Mapping of vegetation traits: RTM
Radiative transfer modeling: “Use of physical laws”
Advantages: - Field data only for validation needed
- More generic (time, landscape)
- Not sensor specific
- Data redundancy not a problem
Jones & Vaugham, 2010
Notes: What is a RTM? … physical description of light interaction with canopy

## Slide 6
Mapping of vegetation traits: RTM
Forward simulation:
Reflectance spectra are simulated outputs
LAI
Notes: 6

## Slide 7
Mapping of vegetation traits: RTM
MODEL
COMPARI- SON
measured spectrum
modelled spectrum
change input parameters
until spectra match
Output:
parameters
at best match
Source: Verhoef, 2005
Model inversion:
Reflectance spectra are inputs; parameters are outputs
Notes: 7

## Slide 8
Numerical optimizations Time consuming and risk of local minima
Mapping of vegetation traits: RTM

## Slide 9
Global search algorithm in spectral space
q
q
q
q
q
synthetic data base
MODEL
RTM
look-up-table (LUT)
neural net (NN)
predictive equation (PE)
Mapping of spectral space onto parameter space q = f(rl)
Non-linear mapping using all wavelengths
Linear mapping using only 2 wavelengths
Alternative approaches ….
Mapping of vegetation traits: RTM

## Slide 10
Mapping of vegetation traits: “Ill-posedness“
Notes: 10
Illposedness in empirical and physical based approaches … also for classical land cover studies

## Slide 11
15 Landsat spectra
Mapping of vegetation traits: “Ill-posedness“
Notes: 11
Illposedness in empirical and physical based approaches

## Slide 12
Mapping of vegetation traits: “Ill-posedness“
Notes: 12
Illposedness in classification approaches

## Slide 13
Sensor improvements
By mapping the Earth surface in many continuous spectral bands, a better inversion of radiative transfer models can be achieved (source: web)
CopinG with Ill-posedness

## Slide 14
Increasing the dimensionality of the data
The ill-posed problem can be considerably reduced by increasing the dimensionality of the data set – here: combining spectral and directional data (source: web)
-60° -45° hot spot nadir view +22° +45° +60°
660 nm, 730 nm, 840 nm
CopinG with Ill-posedness

## Slide 15
Increasing the dimensionality of the data
X-Band
3 cm
C-Band
6 cm
L-Band
23 cm
The ill-posed problem can be considerably reduced by increasing the dimensionality of the data set – here: by combining optical and microwave data sets (source: web)
CopinG with Ill-posedness

## Slide 16
Including (external) prior information
The error surface can be better reshaped and restricted, if externally derived prior information is available (e.g. land cover classification yielding information on plant architecture) (Schlerf, Atzberger & Hill, 2002)
spectral info
prior info
CopinG with Ill-posedness

## Slide 17
Including (external) prior information
The number of variables to be retrieved can be reduced if some variables can be mapped from other EO data (e.g. stem density from orthophotos) (source: Schlerf & Atzberger)
CopinG with Ill-posedness

## Slide 18
Including (external) prior information
The number of variables to be retrieved can be reduced if some variables can be mapped from other EO data (e.g. canopy height and architecture from LIDAR measurements) (source: web)
CopinG with Ill-posedness

## Slide 19
Exploiting the temporal consistency
time
LAI
1st guess
derived prior info
incl. prior info
time
LAI
LAI
CopinG with Ill-posedness

## Slide 20
Optimization of „soil-isolines“ for pixels within 3 x 3 gliding windows, assuming that only LAI shows a remarkable variation within ± 1 pixel
Exploiting spatial
auto-correlation
CopinG with Ill-posedness

## Slide 21
Mapping of vegetation traits: RTM
MODEL
COMPARI- SON
measured spectrum
modelled spectrum
change input parameters
until spectra match
Output:
parameters
at best match
Key decisions:
really want to use RTM ? (requires BoA … alternatives)
which RTM to chose ? (model assumptions / model complexity)
which inversion technique ?
how to quantify „agreement“ ? (cost function / weighting / noise)
Notes: 21

## Slide 22
Before you start using RTM …
Check model assumption !
Specific conditions in forests are considered ?
RTM is able to generate spectra similar to observed ones ?
Identify reasons for “inappropriate” simulations !
RTM problems ?
Problems with data cube ?
Act, if simulations are not fitting the observations !
Discard bands (RTM and/or data cube)
Assign weights

## Slide 23
Major steps when using LUT for RTM Inversion
[1] Generate LUT
What size ? (density/CPU)
Parameters within logical/physical range
Including a priori information (incl. co-variation)
Check that reflectance space is well populated
[2] Find best match(es) !
Ill-posedness is reality
N best solution often better
Do not invert parameters which are already known
[3] Feature reduction & use of prior info!
Discard bands

## Slide 24
Data sets & Model(s)
Majella National Park
Majella National Park
Notes: 24

## Slide 25
Data sets & Model(s)
mod(λ) = f (, LAI, Cab, Cw, ...)
RTM - INFORM
PROSPECT
SAILH
FLIM
Notes: 25

## Slide 26
MODEL TEST - Spectral
Input of field measured model parameter (i.e., Co, LAI, Chl(a+b)) ...
INFORM
INFORM-Validation (forward modeling)
Notes: 26

## Slide 27
MODEL TEST - directional
Spruce
Beech
View zenith angle (º)
Reflectance
medium
young
NIR (780 nm)
Stand age (in years)
Notes: 27

## Slide 28
3. Ill-posedness is a serious problem … however, not only for RTM inversion
2. Be aware of their limits … & try exploit all dimensions (wavelength, direction, space, time …)
1. RTM are very powerful … & not as complicated as often stated
4. Make use of available prior information !
Conclusion
Notes: 28
Four take-aways

## Slide 29
CONTACT
University of Natural Resources
and Life Sciences, Vienna, Austria
Department of Landscape, Spatial
and Infrastructure Sciences
Institute of Surveying, Remote Sensing
and Land Information
Clement ATZBERGER Peter Jordanstraße 82, A-1190 Vienna, Austria
Tel.: +43 1 47654-5100, Fax: +43 1 47654-5143
clement.atzberger@boku.ac.at www.boku.ac.at
Thank you !
Notes: 29